Optimized gradients based on a custom retention time distribution
(64 bit, Ubuntu assumed)

Pasting the retention times in the Text Area
  1. The input parameters would be
    - Paste the retention times from data/custom/rts-identified-peptides.txt

     - Start gradient time → 10
     - End gradient time → 250
     - Start gradient %B→ 2
     - End gradient %B → 40
     - Lag time → 6.2

     - Time step → 2.5
     - Decimals → 1

  1. The optimized gradient that should be obtained is given in the file
    custom-optimized-paste-rts.txt
    The graphical window displaying the result should look as shown below

1. Loading retention times from an input file
  2.1 The input parameters would be
  - Text Area – leave empty
  - Input file: data/custom/rts-identified-peptides.txt
  - Start gradient time → 10
  - End gradient time → 250
  - Start gradient %B→ 2
  - End gradient %B → 40
  - Lag time → 6.2
  - Time step → 5.0
  - Decimals → 2
  2.2 The optimized gradient that should be obtained is given in the file
  custom-optimized-upload-file.txt
  The graphical window displaying the result should look as shown below